## Slide 1: به نام خدا
سیدمحمدحسین حسینی
تکنولوژی BLE و کاربردهای آن
Polwinno
ارائه دهنده:

## Slide 2
How BLE works
BLE layers
ibeacons
Contents

## Slide 3: What is BLE?
Bluetooth Low Energy (BLE) Digital Radio Protocol
Power consumption:
Central and Peripheral
Hub-and-spoke
How BLE Works
BLE 2 mw
wifi 80 mw
4G/LTE 1000 mw

## Slide 4
Advertising
Scanning
Different Advertising and Scanning speed!
Peripheral sends advertising packets
central scans for advertising packets
frequency hopping
Always start with Advertising

## Slide 5
BLE Layers

## Slide 6: 1- Controller Layer
Physical layer
Link layer
Packets
40 channels 37 data 3 advertising
Longest possible packet 376 us 376 bit/s
Required sensitivity -70 dbm
Maximum transmit power 10 dbm (support 15 meters)

## Slide 7
BLE Address types
Host Controller Interface (HCI)
Channels (to start connection)
Packet formats ( Commands, Events, Data)
Flow controller
Sends commands to Controller
receives back events to Host
Exchange Data

## Slide 8: 2- Host
Logical Link and Adaption Protocol (L2CAP)
Attribute Protocol
Signaling channel
Security manager
Multiplexing layer (Three Channels) for different protocols
Segmentation and Reassembling
Attribute Protocol
Attribute:

## Slide 9
Specifies with 128 bit Universally Unique Identifier (UUID)
Profile UUID
Service UUID
Characteristic UUID
Attribute type:
Attribute permissions:
Read/Write/notify Operations
Encryption/Authorization
Generic Attribute Profile (GATT)
notify

## Slide 10
Generic Access Profile (GAP)
Heart Rate Measurement Value
Body Sensor Location
Heart Rate Control Point
Security
Advance Encryption Standard (AES 128 bit)
Temporary Key
Short-term Key
Long Term Key
Identity Resolving Key
Connection signature Key
Broadcaster
Observer
Peripheral
central
Heart Rate Service
Heart Rate Characteristics

## Slide 11: 3- Application
Application triggered by beacons :
Map Replacement
Transit Assistance
Indoor Direction Finding
Where is my car?
Identify Project Objectives
Museum Guides
Retail Store
Ticket Validation
Restaurant Table Pager

## Slide 12
iBeacons
What is iBeacon?
a Bluetooth Low Energy proximity beacon
Apple
high-precision location information
iBeacon Protocol
advertising packet
Proximity UUID (16 bytes)
Major (2 bytes)
Minor (2 bytes)
Measured Power (1 byte)

## Slide 13
ممنون از توجهتان!